--------------------------------------------------------------------------------
---------------------- FAST PLATFORM FILE --------------------------------------
NREL 5.0 MW offshore baseline monopile platform with rigid foundation input properties.
---------------------- FEATURE FLAGS (CONT) ------------------------------------
False       PtfmSgDOF   - Platform horizontal surge translation DOF (flag)
False       PtfmSwDOF   - Platform horizontal sway translation DOF (flag)
False       PtfmHvDOF   - Platform vertical heave translation DOF (flag)
False       PtfmRDOF    - Platform roll tilt rotation DOF (flag)
False       PtfmPDOF    - Platform pitch tilt rotation DOF (flag)
False       PtfmYDOF    - Platform yaw rotation DOF (flag)
---------------------- INITIAL CONDITIONS (CONT) -------------------------------
   0.0      PtfmSurge   - Initial or fixed horizontal surge translational displacement of platform (meters)
   0.0      PtfmSway    - Initial or fixed horizontal sway translational displacement of platform (meters)
   0.0      PtfmHeave   - Initial or fixed vertical heave translational displacement of platform (meters)
   0.0      PtfmRoll    - Initial or fixed roll tilt rotational displacement of platform (degrees)
   0.0      PtfmPitch   - Initial or fixed pitch tilt rotational displacement of platform (degrees)
   0.0      PtfmYaw     - Initial or fixed yaw rotational displacement of platform (degrees)
---------------------- TURBINE CONFIGURATION (CONT) ----------------------------
  56.0      TwrDraft    - Downward distance from the ground level [onshore] or MSL [offshore] to the tower base platform connection (meters)
  56.0      PtfmCM      - Downward distance from the ground level [onshore] or MSL [offshore] to the platform CM (meters)
  56.0      PtfmRef     - Downward distance from the ground level [onshore] or MSL [offshore] to the platform reference point (meters)
---------------------- MASS AND INERTIA (CONT) ---------------------------------
   0.0      PtfmMass    - Platform mass (kg)
   0.0      PtfmRIner   - Platform inertia for roll tilt rotation about the platform CM (kg m^2)
   0.0      PtfmPIner   - Platform inertia for pitch tilt rotation about the platform CM (kg m^2)
   0.0      PtfmYIner   - Platfrom inertia for yaw rotation about the platform CM (kg m^2)
---------------------- PLATFORM (CONT) -----------------------------------------
   0        PtfmLdMod   - Platform loading model {0: none, 1: user-defined from routine UserPtfmLd} (switch)
---------------------- TOWER (CONT) --------------------------------------------
   2        TwrLdMod    - Tower loading model {0: none, 1: Morison's equation, 2: user-defined from routine UserTwrLd} (switch)
   6.0      TwrDiam     - Tower diameter in Morison's equation (meters) [used only when TwrLdMod=1]
   1.0      TwrCA       - Normalized hydrodynamic added mass   coefficient in Morison's equation (-) [used only when TwrLdMod=1] [determines TwrCM=1+TwrCA]
   1.0      TwrCD       - Normalized hydrodynamic viscous drag coefficient in Morison's equation (-) [used only when TwrLdMod=1]
---------------------- WAVES ---------------------------------------------------
   0.0      WtrDens     - Water density (kg/m^3)
  20.0      WtrDpth     - Water depth (meters)
   0        WaveMod     - Incident wave kinematics model {0: none=still water, 1: plane progressive (regular), 2: JONSWAP/Pierson-Moskowitz spectrum (irregular), 3: user-defind spectrum from routine UserWaveSpctrm (irregular), 4: GH Bladed wave data} (switch)
   3        WaveStMod   - Model for stretching incident wave kinematics to instantaneous free surface {0: none=no stretching, 1: vertical stretching, 2: extrapolation stretching, 3: Wheeler stretching} (switch) [unused when WaveMod=0]
3630.0      WaveTMax    - Analysis time for incident wave calculations (sec) [unused when WaveMod=0] [determines WaveDOmega=2Pi/WaveTMax in the IFFT]
   0.25     WaveDT      - Time step for incident wave calculations (sec) [unused when WaveMod=0] [0.1<=WaveDT<=1.0 recommended] [determines WaveOmegaMax=Pi/WaveDT in the IFFT]
   5.0      WaveHs      - Significant wave height of incident waves (meters) [used only when WaveMod=1 or 2]
  12.4      WaveTp      - Peak spectral period of incident waves (sec) [used only when WaveMod=1 or 2]
DEFAULT     WavePkShp   - Peak shape parameter of incident wave spectrum (-) or DEFAULT (unquoted string) [used only when WaveMod=2] [use 1.0 for Pierson-Moskowitz]
   0.0      WaveDir     - Incident wave propagation heading direction (degrees) [unused when WaveMod=0 or 4]
123456789   WaveSeed(1) - First  random seed of incident waves [-2147483648 to 2147483647] (-) [unused when WaveMod=0 or 4]
1011121314  WaveSeed(2) - Second random seed of incident waves [-2147483648 to 2147483647] (-) [unused when WaveMod=0 or 4]
"Dummy"     GHWvFile    - Root name of GH Bladed files containing wave data (quoted string) [used only when WaveMod=4]
---------------------- CURRENT -------------------------------------------------
   0        CurrMod     - Current profile model {0: none=no current, 1: standard, 2: user-defined from routine UserCurrent} (switch)
   0.0      CurrSSV0    - Sub-surface current velocity at still water level (m/s) [used only when CurrMod=1]
DEFAULT     CurrSSDir   - Sub-surface current heading direction (degrees) or DEFAULT (unquoted string) [used only when CurrMod=1]
  20.0      CurrNSRef   - Near-surface current reference depth (meters) [used only when CurrMod=1]
   0.0      CurrNSV0    - Near-surface current velocity at still water level (m/s) [used only when CurrMod=1]
   0.0      CurrNSDir   - Near-surface current heading direction (degrees) [used only when CurrMod=1]
   0.0      CurrDIV     - Depth-independent current velocity (m/s) [used only when CurrMod=1]
   0.0      CurrDIDir   - Depth-independent current heading direction (degrees) [used only when CurrMod=1]
---------------------- OUTPUT (CONT) -------------------------------------------
   0        NWaveKin    - Number of points where the wave kinematics can be output [0 to 9] (-)
   0        WaveKinNd   - List of tower nodes that have wave kinematics sensors [1 to TwrNodes] (-) [unused if NWaveKin=0]